## Slide 1: Smart Energy Aware Systems (SEAS) Outsourcing Electric Vehicle Smartcharging on the web of Data
14/03/2016
EUREKA Innovation Week, 27/04/2016
Maxime Lefrançois (École Nationale Supérieure des Mines) Guillaume Habault (IMT/TELECOM Bretagne)
Caroline Ramondou (CNR)

## Slide 2
Smart Energy Aware Systems (SEAS) project:
Aims at developing an ecosystem to help entities better manage, coordinate and optimize energy consumption, production and storage.
This presentation reports a joint work between SEAS partners and particularly focuses on Compagnie Nationale du Rhône (CNR) Electric Vehicle (EV) Smart Charging Use Case (UC), which tackles the emerging need for electric mobility.
submitted to:
Maxime Lefrançois, Guillaume Habault, Caroline Ramondou and Eric Françon, 2016,
Outsourcing Electric Vehicle Smart Charging on the Web of Data, The First Int. Conf. on Green Communications, Computing and Technologies (GREEN'16), July 24-28, Nice, France

## Slide 3: 1 – Context : the need of EV smartcharging
With smart charging
Without smart charging
EV are charged instantly
No external control is involved in the charging process.
With the expected growth of EV:
Uncontrolled charging introduces fluctuation in energy consumption
Impact on the electricity system:
Distribution grids congestions due to power peaks and voltage drops,
Increased costs of electricity,
Expensive generation and grid reinforcements.
Consequences
Smartcharging is a solution to integrate EV in power system in a user-friendly way
Notes: Currently, Electric Vehicles (EV) are charged instantly when plugged into a charging station and no external control is involved in the charging process.
With the increase of EV expected for the coming years, this uncontrolled charging introducing fluctuation in energy consumption will have an impact on the electricity system.

## Slide 4: 2 – Smart charging solutions
90% of EV charging is expected to occur at home or at the office :
in most cases, these EVs stay parked for several hours
Customer: it might reduce their Electricity costs
DSO : it could assist grid management with control signals
The society: it could avoid grid and generation investments
The environment: it may facilitate integration of renewable energies (e.g. self-consumption of electricity with solar power and electric vehicles);
Benefits
Smartcharging solutions:
Shifting EV charging from peak periods to off-peak periods;
Allow to reduce load peaks.

## Slide 5
3 – A Smart charging Use case in SEAS project
CNR works on a smart charging solution that can address all types of electrical vehicle, charging points, and optimization strategies.
1 - EV Driver
Reports its charging needs
2 - Charging Station Operator
Monitors charging stations and applies optimized chargeplans.
3 - Smart Charging Provider
Provides an optimal chargeplan for each EV based on several inputs (EV Driver requirements, available power, prices signals…)
Battery charge level = Energy (kWh)
Time of departure
= Delay (h)

## Slide 6
EV Driver
Charging Station Operator
Smart Charging Provider
Energy Producer
Energy Retailer
DSO
Contract (based on dynamic pricing)
sourcing
Prices
Charge needs
Charge plans
Charging requests
Monitoring
Metering data
Charging station
EVSE
meter
EVSE
meter
Charging station
EVSE
meter
EVSE
meter
Customer
Energy Markets
4 – The Smart charging process
At any time, the charge plan may be re-optimized by the SCP on CSO requests, especially if new EV charging events occurs (plug/unplug), if an EV Driver modify its requirements, or in case of modification of available power.
Metering Point
Notes: EV Driver is authorized to use a charging station connected to the grid, and managed by a Charging station Operator (CSO). He communicates directly – via his smartphone or a web application – or through the charging station, his requirements : energy needs (related to battery state of charge) and preferences (parking time).
CSO takes these information into account along with several other parameters such as power constraints (limitation of maximum instantaneous power at the delivery point, energy requested by other EV drivers connected to the same area) and asks to the Smart Charging Provider (SCP) for an optimized charge plan.
SCP combines the received information with other data such as prices information (e.g. dynamic hourly price of energy) and control signals (e.g. maximum power demand). It then runs optimization algorithm to settle the EV charge plan, which is a series of consecutive blocks of maximal power value (Pmax) for defined time periods.
CSO, receiving the resulting charge plan from SCP, applies this plan and monitors the charging station in accordance.
EV controls the actual power delivered by the charging station to the battery, which should be lower than the Pmax defined by the charge plan.

## Slide 7
5 – Smartcharging algorithms
CNR is an hydroelectricity producer
Has developed an electricity mixed production (wind, solar, small hydro-power);
Becomes an expert in managing an intermittent energy, by forecasting, optimizing, marketing and supervising production;
Uses its own algorithm to optimize EV consumption according to several strategies.
The smartcharging strategy tested in this UC is based on:
EV requirements;
Available power at Metering Point;
Forecast and day)ahead prices;
Real-time connection of EV at a charging station.
The goal of this optimization approach is to minimize the charging cost without negotiating the charging needs, as the customer satisfaction and the reliability of the charging service have higher priority than the system operating cost.
Example of an optimized EV charging session

## Slide 8
7 – Architecture
SEAS has to define an architecture enabling real-time interconnection of any energy actors.
This interconnection helps:
Actors offer energy dedicated services to other SEAS entities;
Coordinate microgeneration with grid needs and production;
Any entities better manage energy consumption, production and storage.
This architecture should meet some general requirements such as:
Being scalable, adaptable and dynamic;
Offering plug-and-play solutions (having as less manual configuration as possible);
Providing secure communications and privacy of information.
End Node (EN) : EVSE’s meter
End User (EU) : Customer, EV Driver
Area Manager (AM) : CSO
Seas Core Entity (SCE) : SCP, Energy Retailer, Energy Producer, DSO
CNR scenario
Illustration of SEAS Reference Architecture Model

## Slide 9
CNR smart charging service implementation is:
(step 1) A RESTful web service
8 – Implementation
RES: 200 OK, "here is optimized charge plan xyz"
(in legacy XML format)
Available for testing - http://cnr-seas.cloudapp.net/scp/
Charging Station Operator
Smart Charging Provider
REQ: "Here is a new charge need"
(in legacy XML format)
Station info
EVSEs
Charge needs
REQ: "Give me charge plan xyz"
RES: 202 Accepted,
"content will be available at location xyz"

## Slide 10
8 – Implementation + Semantic interoperability
We want to use the W3C Resource Description Framework to enable semantic interoperability
BUT 100% adopting this formalism is (1) sometimes costly, (2) sometimes impossible
we introduce SPARQL Protocol and RDF Generation Language that enables to:
- declaratively write a rule to interpret a document as RDF
- when serving a document with the legacy CNR API, add a link to such a rule
e.g. REQ: "Give me charge plan xyz", response contains Link in HTTP Header:
Link: <http://cnr-seas.cloudapp.net/scp/query/ChargingPlan>;rel="sparql-query";var="message"
(demo)
Hence, legacy APIs can enter the realm of the Semantic Web at drastically lowered costs
Notes: REQ: "Give me charge plan xyz"

## Slide 11
CNR smart charging service implementation is:
(step 1) A RESTful web service
(step 2), uses SPARQL-Generate protocol and is deployed as a RESTful Web Service.
8 – Implementation + Semantic interoperability
Demo http://cnr-seas.cloudapp.net/scp/form.html
RES: 200 OK, "here is optimized charge plan xyz"
(in legacy XML format + Link to SPARQL-Generate query)
Charging Station Operator
Smart Charging Provider
REQ: "Here is a new charge need"
(in legacy XML format)
Station info
EVSEs
Charge needs
REQ: "Give me charge plan xyz"
RES: 202 Accepted,
"content will be available at location xyz"

## Slide 12
This work uses the SEAS ontologies, https://w3id.org/seas/ontology/all#
And the MDQ energy vocabulary https://w3id.org/multidimensional-quantity/resource/EnergyVocabulary
These ontologies are online and follow the best practices of the web of linked vocabularies
-> each resource in the ontology is described at its own URL in different formats for machines and humans
9 – Ontology
https://w3id.org/seas/ontology/all#System
Accept: text/html
Accept: text/turtle
Notes: Pour la démo,

## Slide 13
At its core, we describe and quantify Systems, Connections between these systems, and ConnectionPoints at which connections occur
9 – Ontology
example:
Grid, EV, Ch. Station, are Systems
There is a connection between Grid and Ch Station, Ch. Station and EV
This connection occurs at a connection point of the Ch Station (the EVSE), and of the EV (the plug)
Notes: Pour la démo,

## Slide 14
9 – Ontology
The Multidimensional Quantities (MDQ) ontology enables to represent and reason with physical quantities, time-series, simple aggregations.
The MDQ Energy Vocabulary
- describes quantities for the energy domain,
- is automatically generated from a JSON configuration file using SPARQL-Generate

## Slide 15: Thank you
Maxime Lefrançois, Guillaume Habault, Caroline Ramondou and Eric Françon, 2016, Outsourcing Electric Vehicle Smart Charging on the Web of Data, The First Int. Conf. on Green Communications, Computing and Technologies (GREEN'16), July 24-28, Nice, France (submitted)
Links:
The Demo website - http://cnr-seas.cloudapp.net/scp/
The SEAS project - https://w3id.org/seas
The SEAS ontologies - https://w3id.org/seas/ontology/all# (collaboration with WP2)
The MDQ project - https://w3id.org/multidimensional-quantity
The MDQ ontology - https://w3id.org/multidimensional-quantity/resource/Ontology
The MDQ energy vocabulary- https://w3id.org/multidimensional-quantity/resource/EnergyVocabulary
The SPARQL-Generate project - https://w3id.org/sparql-generate
This presentation - http://cnr-seas.cloudapp.net/scp/presentation.pptx